## Slide 1
路由器的路由功能

## Slide 2
IP数据报
路由选择模块
1.路由表
路由选择处理器
(3.路由选择协议)
IP数据报
2.路由选择算法
路由器的路由选择部分
路由表的构成与查找

## Slide 3: 4.3 路由表的构成与查找
对应课本“4.3节 IP层转发分组的过程”

## Slide 4: 4.3.0 IP数据报的交付方式
一.直接交付:当分组的源主机和目的主机是在同一个网络、或在最后一个路由器与目的主机之间时，进行直接交付。
二.间接交付:目的主机与源主机不在同一 个网络上，IP分组无法直接到达目的主机, 需要经过路由器转发，进行间接交付

## Slide 5
Notes: 为什么在一个以太网以内可以直接交付：通过主机arp模块得到网卡地址，通过交换机送到

## Slide 6
Notes: 一个数据包从源到目的主机，一定经一个直接交付，可能经历一个或多个间接交付。

## Slide 7: 判断:一台主机/路由器X能否将一个IP分组直接交付给目的主机Y,还是需要路由器进行间接交付?
方法:判断X和Y是否在同一个子网中! 如果
在同一个子网中,可以直接交付;不在同一个
子网中,必须间接交付.
Notes: 直接交付，意味着路由器完成任务了

## Slide 8
前缀匹配 | 下一跳
128.1.2.64/26 128.1.2.128/26 128.1.2.192/26 | R2，接口 1 直接，接口 1 直接，接口 0
128.1.2.194
0
128.1.2.193
源主机 H1
子网前缀
128.1.2.192/26
128.1.2.130
R1
1
R2
子网前缀
128.1.2.128/26
目的主机 H2
128.1.2.132
0
1
128.1.2.131
H3
128.1.2.65
子网前缀
128.1.2.64/26
128.1.2.68
N1
N2
N3
R1 的部分转发表
主机 H1 发送出的、目的地址是 128.1.2.132 的分组是如何转发的？
路由器转发分组的举例：

## Slide 9
N1 的 网络地址为 128.1.2.192
N1 的 网络掩码为 /26 = 255.255.255.192
128. 1 . 2 .132
255.255.255.192
128. 1 . 2 .128
目的地址与网络掩码
逐比特 AND
 H1 的网络地址
128.1.2.132 不在本地网络上。
源主机 H1 必须把分组发送给路由器 R1。
H1 首先检查 128.1.2.132 是否连接在本网络上。
如果是，则直接交付；否则，就送交路由器 R1。

## Slide 10
前缀匹配 | 下一跳
128.1.2.64/26 128.1.2.128/26 128.1.2.192/26 | R2，接口 1 直接，接口 1 直接，接口 0
128.1.2.132 AND 255.255.255.192 = 128.1.2.128 不匹配!
128.1.2.194
0
128.1.2.193
源主机 H1
子网前缀
128.1.2.192/26
128.1.2.130
R1
1
R2
子网前缀
128.1.2.128/26
目的主机 H2
128.1.2.132
0
1
128.1.2.131
H3
128.1.2.65
子网前缀
128.1.2.64/26
128.1.2.68
N1
N2
N3
R1 的部分转发表
路由器 R1 收到分组后查找转发表。先检查第 1 行。

## Slide 11
前缀匹配 | 下一跳
128.1.2.64/26 128.1.2.128/26 128.1.2.192/26 | R2，接口 1 直接，接口 1 直接，接口 0
128.1.2.132 AND 255.255.255.192 = 128.1.2.128
第二条匹配! 第三条不匹配！
128.1.2.194
0
128.1.2.193
源主机 H1
子网前缀
128.1.2.192/26
128.1.2.130
R1
1
R2
子网前缀
128.1.2.128/26
目的主机 H2
128.1.2.132
0
1
128.1.2.131
H3
128.1.2.65
子网前缀
128.1.2.64/26
128.1.2.68
N1
N2
N3
R1 的部分转发表
路由器 R1 收到分组后查找转发表。接着检查第 2 行。
进行分组的直接交付（通过路由器 R1 的接口 1）。

## Slide 12: 4.3.1 路由表的构成与查找
一.路由表的构成：
IP路由表中每一条记录是一条路由；
一条路由记录包括四部分：
目的IP地址/前缀长度 下一跳地址 输出接口
目的地址/前缀长度 | 下一跳地址 | 接口
202.197.10.0/24 | 直接传送 | a
202.197.11.0/24 | 直接传送 | c
202.197.12.0/24 | 202.197.11.3 | c
202.197.10.2/32 | 直接传送 | a
0.0.0.0/0 | 202.197.11.2 | c
路由表中只记录下一站地址，并不记录完整的路径！
Notes: 前缀长度的含义：路由器将需要转发的IP分组的目的地址读出，将该目的地址与路由表的一条记录的目的地址从左至右进行逐位的比对，若相同的比特位数大于等于前缀长度，则该条记录的目的地址和将转发的分组目的地址匹配

## Slide 13
二 .路由表中的记录类型:
根据目的地址不同进行分类
1.特定主机路由
2.网络前缀路由
3.默认路由
目的地址/前缀长度 | 下一跳地址 | 接口
202.197.10.0/24 | 直接传送 | a
202.197.11.0/24 | 直接传送 | c
202.197.12.0/24 | 202.197.11.3 | c
202.197.10.2/32 | 直接传送 | a
0.0.0.0/0 | 202.197.11.2 | c
Notes: 前缀长度的含义：路由器将需要转发的IP分组的目的地址读出，将该目的地址与路由表的一条记录的目的地址从左至右进行逐位的比对，若相同的比特位数大于等于前缀长度，则该条记录的目的地址和将转发的分组目的地址匹配

## Slide 14
1.特定主机路由: 目的地址是某一特定主机的IP地址,即前缀长度为32的路由表记录
202.197.10.2/32 直接传送 a
需要对每个可能的目的主机建一条记录，一般用于指定特定服务器用,或者用于网络排错或测试等;

## Slide 15
2.网络前缀路由:把目的主机所在的网络地址作为路由表的目的地址的路由表记录，前缀长度在1-31之间
202.197.10.0/24 直接传送 a
可以减少路由表内容,简化查询过程

## Slide 16
3.默认路由:前缀长度为0的路由表记录，可以匹配任何目的IP地址。
0.0.0.0/0 202.197.11.2 c
一般用于不符合路由表中其他目的地址的数据报所采用的路由,减少路由表的占用空间,加快处理速度

## Slide 17: 三.路由匹配规则——如何查路由表
如何命中一条记录？----路由匹配计算
即IP分组目的地址与每一条路由的前缀长度对应的网络掩码进行与运算,如果得到的结果和该记录的目的地址一致,则匹配该记录
若有多条路由表项匹配，选择匹配的前缀长度最长的表项。
Notes: 或者:目的地址与前缀长度对应的网络掩码进行与运算,如果得到的结果和目的地址一致,则匹配该记录

## Slide 18: 路由表匹配规则举例
目的地址/前缀长度 | 下一跳地址 | 接口
202.197.10.0/24 | 直接传送 | a
202.197.11.0/24 | 直接传送 | c
202.197.12.0/24 | 202.197.11.3 | c
202.197.10.2/32 | 直接传送 | a
0.0.0.0/0 | 202.197.11.2 | c
IP目的地址：202.197.10.2；202.197.11.7；202.197.13.5

## Slide 19: 路由表匹配规则举例—查询效率
目的地址/前缀长度 | 下一跳地址 | 接口
202.197.10.2/32 | 直接传送 | a
202.197.11.0/24 | 直接传送 | c
202.197.12.0/24 | 202.197.11.3 | c
202.197.10.0/24 | 直接传送 | a
0.0.0.0/0 | 202.197.11.2 | c
IP目的地址：202.197.10.2；202.197.11.7；202.197.13.5

## Slide 20: 最长前缀匹配规则
在查找路由表时可能会得到不止一个匹配结果。
应当从匹配结果中选择具有最长网络前缀的路由----最长前缀匹配规则
因为网络前缀越长，其地址块就越小，因而路由就越具体 。

## Slide 21: 最长前缀匹配举例
收到的分组的目的地址 D = 206.0.71.129
路由表中的项目：206.0.68.0/22 （ISP）
206.0.71.128/25 （四系）
查找路由表中的第 1 个项目
AND D = 206. 0. 01000111.10000001
第 1 个项目 206.0.68.0/22 的掩码 M 有 22 个连续的 1。
M = 11111111 11111111 11111100 00000000
因此只需把 D 的第 3 个字节转换成二进制。
M = 11111111 11111111 11111100 00000000
206. 0. 01000100. 0
与 206.0.68.0/22 匹配

## Slide 22: 最长前缀匹配举例
收到的分组的目的地址 D = 206.0.71.129
路由表中的项目：206.0.68.0/22 （ISP）
206.0.71.128/25 （四系）
再查找路由表中的第 2 个项目
AND D = 206. 0. 71. 10000001
第 2 个项目 206.0.71.128/25 的掩码 M 有 25 个连续的 1。
M = 11111111 11111111 11111111 10000000
因此只需把 D 的第 4 个字节转换成二进制。
M = 11111111 11111111 11111111 10000000
206. 0. 71. 10000000
与 206.0.71.128/25 匹配

## Slide 23: 最长前缀匹配
D AND (11111111 11111111 11111100 00000000)
= 206.0.68.0/22 匹配
D AND (11111111 11111111 11111111 10000000)
= 206.0.71.128/25 匹配
选择两个匹配的地址中更具体的一个，即选择最长前缀的地址。

## Slide 24: 总结:路由匹配规则
如何命中一条记录？----路由匹配计算
即IP分组目的地址与每条路由的前缀长度对应的网络掩码进行与运算,如果得到的结果和该记录的目的地址一致,则匹配该记录
若有多条路由表项匹配，选择匹配的前缀长度最长的表项。
Notes: 或者:目的地址与前缀长度对应的网络掩码进行与运算,如果得到的结果和目的地址一致,则匹配该记录

## Slide 25
路由器分组转发算法 P144
提取分组的目的地址 IP 地址 D
找到 D 的特定主机路由 ？
找到 D 的最长前缀匹配 ？
找到默认路由？
转发分组到下一跳路由器
丢弃分组，报错
查找路由表
是
否
否
否
是
是
假定路由表条目按照网络前缀的长短排列，前
缀长的在前：
Notes: 本方法是最基本的查找路由的方法，但是查找次数太多。
当路由表中条目较多，如何缩短查找路由表的时间？

## Slide 26: 练习
设某路由器建立了如下路由表：
目的网络 子网掩码 下一跳
202.32.75.0 255.255.255.128 f0/0
202.32.75.128 255.255.255.128 s2/0
118.96.40.0 255.255.255.128 f0/2
198.4.153.0 255.255.255.192 s3/0
0.0.0.0(默认) 0.0.0.0 f0/0
现收到四个分组，其目的地址分别为：
①202.32.75.160 ②198.4.153.17 ③198.4.153.90
④201.35.64.3, 试分别计算出下一跳
Notes: 2455

## Slide 27: 补充：路由器学习路由信息的三种途径 1、直连路由：路由器可以自行学到 2、静态路由 由网络管理员在路由器上手工添加路由信息以实现路由目的动态路由 3、动态路由 由动态路由选择协议自动生成，且根据网络结构或流量的变化，路由协议会自动调整路由信息
Notes: Purpose: This figure introduces students to static and dynamic routes.
Emphasize:
Static knowledge is administered manually—A network administrator enters it into the router’s configuration. The administrator must manually update this static route entry whenever an internetwork topology change requires an update. Static knowledge can be private—by default it is not conveyed to other routers as part of an update process. You can, however, configure the router to share this knowledge.
Dynamic knowledge works differently. After the network administrator enters configuration commands to start dynamic routing, route knowledge is updated automatically by a routing process. Whenever new topology information is received from the internetwork, routers update neighbors about the route change.

## Slide 28: 思科路由器静态路由的配置
  指定一条可以到达目标网络的路径
Router(config)#ip route destination-network [mask] {next-hop address | interface}[administrative-distance] [permanent]
Notes: Purpose: This figure describes the command syntax used to establish an IP static route.
Emphasize: A static route allows manual configuration of the routing table. No dynamic changes to this table entry will occur as long as the path is active. Routing updates are not sent on a link that is only defined by a static route; hence, conserving bandwidth.
Describe the The ip route field descriptions:
    network—destination network or subnet
    mask—subnet mask
    address—IP address of next hop router
    interface—name of interface to use to get to destination network.
Transition: The next figure provides a static route configuration example.

## Slide 29: 静态路由的例子
ip route 172.16.1.0 255.255.255.0 172.16.2.1
172.16.2.1
S0
172.16.1.0
B
172.16.2.2
Network
A
B
ip route 172.16.1.0 255.255.255.0 s0
真题2009
问题：路由器B上的静态路由如何配置？
Notes: Purpose: This figure gives an example of a static route configuration.